## Slide 1
Main controller design
GAM.PHI Internal Project
27 Apr 2023

## Slide 2
CONTENT
2
Main application flowchart
1
Overview
1
3
CAN library API specification
© Copyright FPT Software – Level of Confidentiality
4
Improvements and Limitations

## Slide 3
01. Overview

## Slide 4: Overview
The purpose of this document is to describe the main controller’s main application as well as state the current limitations and future improvements for the RC Car project

## Slide 5
02. Main application flowchart

## Slide 6: Flowchart
Set pin p9.19 to CAN
Set pin p9.20 to CAN
Start
Initialize Socket CAN
Init = OK
End
pthread_create(Task1)
pthread_join(Task1)
True
ReceiveMessage
false
true
true
Success?
Success?
true
true
false
false

## Slide 7
03. CAN library API specification

## Slide 8: CAN Library
CAN Library Definitions:
Name | Value | Description
MAIN_CTRL_ID | 0x000U | Main ECU CAN ID
ECU1_CAN_ID | 0x011U | ECU 1 CAN ID
ECU2_CAN_ID | 0x022U | ECU 2 CAN ID
MAIN_CONTROL_BASE_ADDR | 0x00U | Main control base address ID
CRASH_DETECT_NOTIFY | 0x00U | Crash detection notify ID
ULTRASONIC_BASE_ADDR | 0x01U | Ultrasonic base address ID
GET_DISTANCE_1 | 0x00U | Sensor 1 ID
GET_DISTANCE_2 | 0x01U | Sensor 2 ID
GET_DISTANCE_3 | 0x02U | Sensor 3 ID

## Slide 9: CAN Library
CAN Library APIs:
CanInit()
CanRead()
CanWrite()
CAN Library Definitions:
Name | Value | Description
LED_BASE_ADDR | 0x02U | LED base address ID
TOGGLE_R_TURN_SIGNAL_ADDR | 0x00U | LED right turn address ID
TOGGLE_L_TURN_SIGNAL_ADDR | 0x01U | LED left turn address ID
TOGGLE_BRAKE_LIGHT_ADDR | 0x02U | LED brake address ID
TOGGLE_HEAD_LIGHT_ADDR | 0x03U | LED headlights address ID
TOGGLE_REVERSE_LIGHT_ADDR | 0x04U | LED reverse light address ID

## Slide 10: CAN Library
CAN Library Definitions:
Name | Value | Description
AIRBAG_BASE_ADDR | 0x03U | Airbag base address ID
AIRBAG_SET_OFF | 0x00U | Airbag set off ID
SERVO_BASE_ADDR | 0x04U | Servo base address ID
SET_STEERING_ANGLE | 0x00U | Set steering angle ID
SET_STEERING_STRAIGHT | 0x01U | Set steering angle straight ID
SPEED_MOTOR_BASE_ADDR | 0x05U | Speed motor base address ID
SET_SPEED | 0x00U | Set speed ID
SET_MOTOR_DIRECTION | 0x01U | Set motor direction speed ID
ENABLE_MOTOR | 0x02U | Enable motor ID
SPEEDOMETER_BASE_ADDR | 0x06U | Speedometer base address ID
GET_SPEED | 0x00U | Get speed ID

## Slide 11: CAN Library
CAN Library APIs:
CanInit()
Function name | CanInit | 
Description | Initialize socket CAN connection | 
Parameter | const int8_t *CanIF | CAN interface name: can0 can1
Return | RET | Return ERROR_OK on success Non-zero on error (refer to error types definition)

## Slide 12: CAN Library
CAN Library APIs:
CanRead()
Function name | CanRead | 
Description | Read socket CAN frame ID and 8 byte data | 
Parameter | struct can_frame *Frame | Pointer to Socket CAN frame data type
Return | RET | Return ERROR_OK on success Non-zero on error (refer to error types definition)

## Slide 13: CAN Library
CAN Library APIs:
CanWrite()
Function name | CanInit | 
Description | Write socket CAN frame ID and 8 byte data | 
Parameter | const struct can_frame Frame | Socket CAN frame data type
Return | RET | Return ERROR_OK on success Non-zero on error (refer to error types definition)

## Slide 14
04. Improvements and Limitations

## Slide 15: Improvements and Limitations
Limitations
Control inputs are hard coded for simulation purpose
Airbag module is not available yet, use LED instead for crash detection
Accelerometer module is not yet available
Improvements
Linux CAN driver will conform to AUTOSAR’s standard
Include Bluetooth module for controller inputs (If supported by Beagle bone black)

## Slide 16
CONTACT US
FPT Cau Giay Building, Duy Tan Street, Dich Vong Hau Ward, Cau Giay District, Hanoi City, Vietnam Tel.: +84 (24) 3 768 9048 Fax: +84 (24) 3 768 9049